## Slide 1
HUMS · A PERVITITCH STUDY
Pervititch
1923 / 1938 · Block 147
From paper to digital city —
the story of one Kadıköy block and its century of transformation.
OPEN THE LIVE 3D MODEL
hums.ilkeryoru.com
scan with your phone — rotate the LOD3 model live
İlker Yörü
CTO, Mindra · ilkeryoru.com
10 minutes · 10 slides · 1 city block
Kadıköy · İstanbul · 2026

## Slide 2
SLIDE 02 · THE ARCHIVE
A paper photograph of an era
Jacques Pervititch · Fire-insurance maps of İstanbul · 1922–1945
1938 · Kadıköy 1:500 · plate 08 (SALT Research)
PER PARCEL
Wall material (stone / brick / wood), storey count, vault type (V.F. = Voûte Française, V.T. = Voûte Turque), openings, even courtyard trees.
PURPOSE
Not an art object — risk classification for fire-insurance underwriters. Every line is data.
WHY IT MATTERS
The most detailed surviving record of early-Republican İstanbul — block by block.
FOR HUMS
Each parcel arrives carrying its own BIM seed: material, height, roof pitch, opening pattern.
HUMS · Block 147 · LOD3 BIM
Refs: R-A1 · R-A2 · R-J4
2 / 11

## Slide 3
SLIDE 03 · THE BLOCK
Block 147 · The heart of Kadıköy Market
Osmanağa neighbourhood · today: Yasa Cd. × Mühürdar Cd.
1938 · Block 147 with neighbours (143–148)
46×52
metres
1,372
square metres
34
parcels modeled
21
KML footprints
Anchor
Hagia Euphemia Greek-Orthodox Church — building 1694, present form 1830
Pervititch street names
“Söğütlü Çeşme Cad.” (W) · “İsmail Sok.” (E) · italic French legend (V.F., V.T., Mg., Tt.)
Why this grid exists
14 Aug 1855 — Kadıköy fire burns ~400 buildings. In 1856 engineer Hasan Tahsin Efendi lays the Ottoman Empire’s first modern orthogonal plan over this exact ground. Mühürdar Cd. is its main axis.
The pages we use
1923 sheet (raw working file) and 1938 sheet (Kadıköy 1:500 · plate 08 · SALT Research).
HUMS · Block 147 · LOD3 BIM
Refs: R-A1 · R-A2 · R-B1 · R-D1 · R-D3
3 / 11

## Slide 4
SLIDE 04 · HERO
Transformation · 100 years around one block
Demography and architecture, in lockstep — 1925 → 2026
1925
Greek-Orthodox
population
≈ 100,000
1942
Wealth Tax
(Varlık Vergisi)
1955
6–7 September
Istanbul pogrom
4,214 homes · 73 churches
1964
≈ 12,000 Greek
citizens deported
1965
Condominium Law
→ apartmentisation
1973
1st Bosphorus Bridge
→ construction boom
2006
Greek-Orthodox
pop. ≈ 2,500
(2.5% of 1925)
2022
Heritage Board
Decision 9900
87 ha Urban Site
2026
HUMS · Block 147
LOD3 BIM live
−97.5%
Istanbul Greek-Orthodox population, 1925 → 2006
73 / 73
Istanbul Greek-Orthodox churches damaged, 1955
87 ha
Kadıköy Market designated Urban Site, 28 Sept 2022
HUMS · Block 147 · LOD3 BIM
Refs: R-E1 · R-F1 · R-F2 · R-G1 · R-G3 · R-H1 · R-I1
4 / 11

## Slide 5
SLIDE 05 · MEMORY INVENTORY
What survived · What was lost
One block · 1,372 m² · 100 years
SURVIVED
Hagia Euphemia Church
1694 / 1830 · still active
Beyaz Fırın
founded 1920 · 5th generation
Akveren Pasta
founded 1925 · 4th generation
Kurukahveci Mehmet Efendi
brand 1871 · Kadıköy branch
Çeşme (fountain)
parcel 39/2 · in place
The 1856 grid plan
Hasan Tahsin Efendi’s axis
LOST / CHANGED
×
Yellow (wooden) parcels
Class C timber shops: (40), (42), (4)+(4a), (39)
×
19th-c. shop-house typology
small ground-floor magasins with V.T. vaults
×
Greek-Orthodox neighbours
Pervititch-era Rum population evaporated
×
Greek-script signage
shop fronts re-lettered post-1955
×
Pervititch street names
“Söğütlü Çeşme Cd.” → Yasa Cd. · “T…L Sok.” → Söğütlüçeşme Cd.
×
Inner-yard timber & cumbas
wooden cantilevers and (4a) inner-court galleries gone
HUMS · Block 147 · LOD3 BIM
Refs: R-B1 · R-C1–C9 · R-D2 · R-H2
5 / 11

## Slide 6
SLIDE 06 · THE REGISTER
The heritage register confirms it
İBB · harita.istanbul · cultural-heritage layer · 2024
Block 147 · centroid 40.99077 N · 29.02521 E · harita.istanbul layer k123 · © İBB 2024
LEGEND · WHAT THE COLOURS MEAN
Hagia Euphemia · church body
olive green
Hagia Euphemia · müştemilat (annex)
amber
Çeşme (fountain) · parcel 39/2
cyan
Registered masonry buildings (Kâgir)
brick red
≈ 85 %
of Block 147 is individually registered as immovable cultural property — not just inside the 2022 urban-site perimeter.
By name
the register lists “Kâgir Fırın Ve Apartman” (Beyaz Fırın block) and “Kuru Kahveci Mehmet Efendi” explicitly.
Annex too
the church müştemilat is registered separately — a level of granularity the 1923 Pervititch sheet already anticipated with its “Enclos” notation.
HUMS · Block 147 · LOD3 BIM
Refs: R-I1 · R-I2
6 / 11

## Slide 7
SLIDE 07 · SURVIVOR #1
Hagia Euphemia · the martyr of Chalcedon
Greek-Orthodox Church · 1694 / 1830 · re-opened 1 April 1993
1923 · Pervititch · church footprint · “Enclos” saw-toothed wall, central dome, Clocher
today · saffron courtyard wall, white gate · CC-BY-SA · Wikimedia Commons
Building biography
451
Council of Chalcedon — Khalkedon = Kadıköy. The saint of this city.
1694
Metropolitan Gabriel rebuilds the church on the site of a Byzantine monastery.
1830
Metropolitan Zacharias II enlarges it with Russian-collected donations — present form.
1955
All 73 Greek-Orthodox churches in İstanbul damaged during the 6–7 September pogrom.
1 Apr 1993
Metropolitan Joachim III restoration · re-consecration.
PERVITITCH CODES ON THIS PARCEL
Tt. tiled roof · 1=2 full-height nave · 2p two partial floors · 1er V.T. Turkish vault · central dome · Enclos saw-toothed yard wall.
HUMS · Block 147 · LOD3 BIM
Refs: R-B1 · R-B2 · R-B3 · R-F1
7 / 11

## Slide 8
SLIDE 08 · SURVIVOR #2
One corner · three brands · 100+ years
Pervititch records a single FİRİN — today three institutions still trade there
Pervititch 1923 · NW corner · parcel (40) “FİRİN”, parcels (34)(36) “Fırın”
STREET-NAME MIGRATION
“Söğütlü Çeşme Cad.” → Yasa Cd.
“T…L Sok.” → Söğütlüçeşme Cd.
1920
Beyaz Fırın
Stoyanof family · Bulgarian-Macedonian Orthodox · 5th generation
On the map: westernmost magasin on the W façade (~10 m²)
Today: Yasa Cd. 23, Osmanağa Mh., Kadıköy [R-C1 · R-C2 · R-C4]
1925
Akveren Makarna
founded by Mehmet Coşkunsu · 4th generation in same building
On the map: parcel (40)/(42) north façade — under the large FİRİN label
Today: Söğütlüçeşme Cd. 12/1 [R-C5]
1871
Kurukahveci Mehmet Efendi
brand opened in Eminönü Spice Bazaar · Kadıköy branch after 1934
On the map: next-door north façade · post-Republic expansion store
Today: Söğütlüçeşme Cd. 12/1, 40.990911 N · 29.025160 E [R-C6 · R-C7 · R-C9]
HUMS · Block 147 · LOD3 BIM
Refs: R-C1 · R-C2 · R-C4 · R-C5 · R-C6 · R-C7 · R-C9 · R-I2
8 / 11

## Slide 9
SLIDE 09 · METHOD
From paper to LOD3 BIM
A reproducible pipeline · one block today, one atlas tomorrow
STAGE 1
1938 Pervititch
raster (TIF)
georeferenced
STAGE 2
21 KML
footprints
1,372 m² block
STAGE 3
buildings.json
34 parcels · LOD3
material + vault
STAGE 4
block147.glb
model-viewer
WebGL · CC-BY
STAGE 5
IFC
BIM downstream
interop
LOD3 means
every façade, opening, vault, roof pitch is its own mesh element — not a textured box.
Block 147 is a lab
the same workflow scales to every Pervititch plate — and to other cities.
Open on your phone
hums.ilkeryoru.com · WebGL model-viewer · annotated parcel data sheets.
HUMS · Block 147 · LOD3 BIM
Refs: R-J1 · R-J2 · R-J3 · R-A2
9 / 11

## Slide 10
TAKE IT WITH YOU
hums.ilkeryoru.com
Rotate the model on your phone · open the parcel data sheets · ask questions.
THANK YOU
İlker Yörü · CTO, Mindra · ilkeryoru.com · Kadıköy · İstanbul · 2026

## Slide 11
SLIDE 11 · SOURCES
Sources & References
A · Archive (Pervititch)
[R-A1] SALT Research — Pervititch atlas · Kadıköy 1:500 plate 08 (1938). archives.saltresearch.org
[R-A2] HUMS repository — georeferenced raster 500_1938_APLPEKADI08.tif. github.com/1lker/hums-project
[R-J4] Toplumsal Tarih Akademi — “1922 Öncesinde Jacques Pervititch.” dergipark.org.tr
B · Hagia Euphemia Church
[R-B1] İstanbul Ansiklopedisi · “AYİA EFİMİA RUM ORTODOKS KİLİSESİ.”
[R-B2] Tarihi İstanbul · Ayia Efimia Rum Ortodoks Kilisesi.
[R-B3] Wikimedia Commons · Category: Saint Euphemia Greek-Orthodox Church (CC-BY-SA).
C · Living brands (1871–1925)
[R-C1] Beyaz Fırın · founded 1920 · Stoyanof family. beyazfirin.com
[R-C5] Akveren Makarna · founded 1925 · Coşkunsu family. akveren.com
[R-C6] Kurukahveci Mehmet Efendi · founded 1871. mehmetefendi.com
D · Kadıköy urban history
[R-D1] Pınar Erkan · “1855 Kadıköy Fire and the First Grid Plan” · Gazete Kadıköy.
[R-D4] Kadıköy Kaymakamlığı · “Geçmişin Modern Mimarisi.”
[R-D5] Arkitera · “Geçmişin Modern Mimarisi — 1: Kadıköy.”
E–H · Demography & politics
[R-E1] Wealth Tax · Wikipedia (TR) — Varlık Vergisi.
[R-F1] 6–7 Sept 1955 pogrom · Wikipedia (TR) — 6-7 Eylül Olayları.
[R-F2] İHD report · 6–7 Eylül 1955 · ihd.org.tr
[R-G1] Greeks of Istanbul / 1964 deportation · Wikipedia (TR).
I–J · Site status & HUMS
[R-I1] İBB Şehir Planlama · Kadıköy Merkez Sit Alanı · Decision 9900 · 28 Sept 2022 · 87 ha.
[R-I2] İBB harita.istanbul · cultural-heritage layer · harita.istanbul/2d/layer/k123 (2024).
[R-J1] HUMS live viewer · hums.ilkeryoru.com
[R-J2] Block 147 LOD3 dataset · buildings.json (34 parcels) + 21 KML footprints.
HUMS · Block 147 · LOD3 BIM
Refs: Full reference list — see §6 of the prompt package
11 / 11